Name: ____________________ (     )	Class: ____________________

Volume and Surface Area of Prism

Question 1:

The following diagram is an open container which has a uniform cross-section.

- Find, in cm2, the total surface area of the container.

- A tap is used to fill up the container with water, at a rate of 0.8 litres per minute.
Calculate the time taken, in minutes, to fill up half the container.

[Answer Key]

(a)  6476 cm2         (b)  24.15 min

Solution

Cross-sectional area/ Base Area

Perimeter of Base Area

= 43+36+17+12+14+12+12+36

=182 cm

Total surface area of container

Vol. of container

= 1380 x 28

= 38 640 cm3

= 38.64 litres

Time taken

Question 2:

A C-shaped block with thickness of 5m is as shown below.  Find

- the total surface area, and

- the volume of the block.

[Take  to be ]

[Answer Key]

(a)  240 m2          (b)

[Solution]

(a)  Front and back surface area

# Inner and outer curved surface area

# Rectangular surface area

(b)

Question 3:

The diagram shows a solid cylinder with a round hole.  The diameter of the base of the

cylinder is 10 cm and its height is 25 cm.  The round hole of radius 5 cm runs from the

top to the centre of the cylinder.  Find the volume and total surface area of the solid.

[Answer Key]

Volume = 6870 cm3, Surface area = 1340 cm2

[Solution]

Question 4:

A closed storage container consists of a cuboid, to which a quadrant of a cylinder is

attached as shown in the diagram below.  AE = 20 cm, ED = 30 cm, DC = 20 cm and

CR = 70 cm.  Taking  to be 3.142, calculate

- the volume of the container,

- the area of the curved surface BQRC,

- the total surface area of the container.

[Answer Key]

(a)  63994 cm3           (b)  2199.4 cm2          (c)  11027.8 cm2

[Solution]

(a)  Cross-sectional area

(b)

(c)

Question 5:

The solid consists of a trapezoidal prism with a cylindrical hole of radius  20 cm in the

centre. AB = 35 cm, EF = 85 cm, FG = 28 cm, CF = DE = 84 cm and the height of the

solid is 80 cm.

- Taking  to be 3.142, calculate the:

- total volume of the solid,

- total surface area of the solid.

- The solid is melted and recast into a cylindrical solid of height 80 cm, find the radius
of the solid.

[Answer Key]

(a)  (i)  99 200 cm3          (ii)  18700 cm2          (b)  19.9 cm

[Solution]

(a)

(b)

(c)

# Text boxes

C

B

84 cm

E

H

D

A

20 cm

80 cm

35 cm

28 cm

85 cm

F

G

20 cm

30 cm

20 cm

70 cm

T

S

R

Q

P

E

D

C

B

A

25 cm

5 cm

10 cm

2 m

4 m

2 m

5 m

36 cm

43 cm

12 cm

12 cm

17 cm

28 cm